## Slide 1: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center 3rd Annual MABAS-Wisconsin Command & Dispatch Conference August 23, 2013
Randall Pickering
MABAS-Wisconsin Communications Committee
WISCOM SSMG/Executive Board

## Slide 2: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Program Objectives
Understand “Operability” and “Interoperability”
Understand the differences between MABAS “Tactical”, “Response” and “Widearea” radio channels
Understand the proper uses of MABAS radio channels
Understand how to sector hot zone radio communications
Understand what narrowbanding is, and how it can affect you
Understand the difference between analog and digital communications channels, and how they can affect you
Understand the role and function of the Badger RED Center

## Slide 3: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understanding “Operability” and “Interoperability”
“Operability” is defined as being able to communicate with your normal, day-to-day service delivery partners.
Operability is usually not the problem
“Interoperability” is defined as being able to communicate with those service delivery partners you don’t normally communicate with:
  Fire/EMS units from other counties and/or other states
  Allied service partners like law enforcement, USAR, Public Works, etc.

## Slide 4: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understanding “Operability” and “Interoperability”
 | Day-to-Day “Local Alarms” | Intradivisional MABAS Alarms | Statewide Coordination | National Response
Fire Service | Local channels / * | MABAS channels | WISCOM channels | V-Call*/ V-TAC*/ IR channels
EMS | Local channels | MABAS channels | WISCOM channels | V-Call*/V-TAC*/IR channels
Support Resources (Haz-Mat, USAR) | Local channels | MABAS channels | WISCOM channels | V-Call*/V-TAC*/IR channels
Allied Services (Law, PW, etc.) | Local / MARC / WISCOM channels | MARC / WISCOM channels | WISCOM Channels | V-Call*/V-TAC*/IR channels

## Slide 5: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understanding the differences between MABAS Tactical / Response / Widearea radio channels
“Tactical” radio channels (Local channels or MABAS “Color” channels)
  On Scene / Hot Zone communications
  Reasonably short distance (Depending on the size/scope of the incident)
  Unit/IC-to-Unit/IC
  Direct radio-to-radio
“Response” radio channels
“Widearea” radio channels

## Slide 6: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understanding the differences between MABAS Tactical / Response / Widearea radio channels
“Tactical” radio channels
“Response” radio channels (IFERN or IFERN2)
  Dispatch / Alerting communications
  Dispatch-to-Dispatch
  Field Units Responding (Intradivisional) / In Staging / Returning to Quarters
  IC-to-Staging / Staging-to-IC
“Widearea” radio channels

## Slide 7: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understanding the differences between MABAS Tactical / Response / Widearea radio channels
“Tactical” radio channels
“Response” radio channels
“Widearea” (WISCOM) radio channels
  Every use will end with the phrase, ….. when normal radio channels will not carry far enough to work [think “interdivisional /task force/strike team responses”]
  Dispatch-to-Dispatch
  Field Units Responding (Interdivisional) / In Staging / Returning to Quarters
  Interdivisional TF/ST Leader-to-Staging / Staging-to-TF/ST Leader

## Slide 8: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Use of Tactical / Response / Widearea radio channels
The use of all MABAS radio channels is described in the following MABAS-Wisconsin POLICIES, PROCEDURES & GUIDELINES:
  C-01.01.01 – VHF Interoperability
  C-01-01.03 – Use of the IFERN and IFERN2 Frequencies
  C-01-02.01 – Wisconsin Statewide Radio License
  C-01-02-03 – Wisconsin Statewide Radio License, 800 MHz TAC Frequencies
  C-01-05.02 – Wisconsin Tactical Frequency Usage
  C-01-06.03 – Transmit Power Limitation

## Slide 9: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Use of Tactical / Response / Widearea radio channels
C-01.01.01 - VHF interoperability
  “Fire Departments rely heavily on two-way radios to communicate between companies, departments, and other disciplines at emergency and disaster scenes. Fire Departments utilize radio frequencies in the VHF-Low, VHF-High, UHF, and 800 MHz frequency bands for day-to-day operations. Newer technologies include the use of analog and digital transmissions and trunking technologies using incompatible protocols.
  While these systems may meet routine needs of individual departments, experience has shown that lack of interoperability between companies operating at an emergency scene can lead to serious and potentially life threatening consequences.
  The FCC’s national radio frequency band plan specifies VHF high band radio frequencies for fire service interoperability and fireground operations.

## Slide 10: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Use of Tactical / Response / Widearea radio channels
C-01.01.01 - VHF interoperability
  This issue is also addressed in WEM 8, paragraph 8.06 – Communications
  “To facilitate radio interoperability during emergency response operations, designated MABAS VHF radio frequencies will be utilized by MABAS member units for on scene communications with MABAS mutual aid partners. This does not preclude fire, rescue and emergency medical services from utilizing other radio frequencies or radio bands for their own internal communications.”

## Slide 11: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Use of Tactical / Response / Widearea radio channels
C-01.01.01 - VHF interoperability
  “Department that utilize frequencies other than VHF high band for primary operations have developed various systems to communicate with MABAS departments at mutual aid calls. These systems have limitations, have tendencies to cause harmful interference, limit operating areas, may violate FCC rules, and could jeopardize the safety of personnel at emergency scenes. The MABAS-Wisconsin Radio Committee has acknowledged that the use of cross band repeaters to be appropriate for use in Wisconsin to link analog fire ground frequencies from two different radio bands together for interoperability at a scene under control of the local incident commander (IC) of the stricken community.”

## Slide 12: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Use of Tactical / Response / Widearea radio channels
“Tactical” radio channels
  On Scene / Hot Zone communications
  Licensed statewide by the State of Wisconsin. No individual radio licenses are required
  Mobile-only operation. No base stations are allowed on the MABAS tactical channels
  MABAS Box Alarms: FG-Red, FG-White, FG-Blue,
  FG-Gold, FG-Black, FG-Gray
  8TAC-Red, 8TAC-White, 8TAC-Blue
  (Intra-state Inter-disciplinary use): MARC-2, MARC-3, MARC-4
  (Interstate / Nationwide use): V-TAC1, V-TAC2, V-TAC3

## Slide 13: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Use of Tactical / Response / Widearea radio channels
“Response” radio channels
  Dispatch / Alerting communications
  Coordination of responding units to the emergency scene or staging area
  Coordination of staging area, including communications between IC-staging
  Routine updates, reports and/or requests for additional resources
  Communications between IC and the MABAS Dispatch Center
  Change of Quarters units
  MABAS Box Alarms: IFERN, IFERN2
  (Intra-state Inter-disciplinary use): MARC-1
  (Interstate / Nationwide use): V-Call

## Slide 14: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Use of Tactical / Response / Widearea radio channels
  “Widearea” (WISCOM) radio channels – aka: when normal radio channels will not carry far enough to work [think “interdivisional /task force/strike team responses”]
  Contact and coordination with MABAS Badger RED Center
  Coordination of units from a wide geographic area responding to a marshaling area
  Coordination by a Inter-divisional Strike Team or Task Force Team Leader with Staging or Reception Area.
  Communications between MABAS and WEM Resources and Coordinators
  MABAS Box Alarms: MABAS1, MABAS2

## Slide 15: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
How to sector hot zone radio communications
Unit Assignment | Routine Local Incidents | MABAS Incidents | Alternative
HOT ZONE: |  |  | 
Scene (Hot Zone) 1st Due Companies | Local FG or RED | RED | GOLD
Interior Companies | Local FG or RED | RED | GOLD
Safety Officer / Team | Local FG or RED | RED | GOLD
R I T | Local FG or RED | RED | GOLD
Accountability | Local FG or RED | RED | GOLD
Extrication Group | Local FG or RED | RED | GOLD
Water Supply | LOCAL or BLUE | BLUE | GRAY
Relay Pumping | LOCAL or BLUE | BLUE | GRAY
Master Stream Operations | LOCAL or BLUE | BLUE | GRAY

## Slide 16: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
How to sector hot zone radio communications
Unit Assignment | Routine Local Incidents | MABAS Incidents | Alternative
SUPPORT FUNCTIONS: |  |  | 
Logistics Officer | LOCAL or WHITE | WHITE | BLACK
P I O | LOCAL or WHITE | WHITE | BLACK
Liaison Officer | LOCAL or WHITE | WHITE | BLACK
Plans Chief | LOCAL or WHITE | WHITE | BLACK
Support Functions | LOCAL or WHITE | WHITE | BLACK

## Slide 17: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
How to sector hot zone radio communications
Unit Assignment | Routine Local Incidents | MABAS Incidents | Alternative
EMS OPERATIONS: |  |  | 
EMS Operations | LOCAL or EMS C | EMS C | Wiscom EMS
Triage Group Supervisor | LOCAL or EMS C | EMS C | MARC 2-4
Treatment Group Supervisor | LOCAL or EMS C | EMS C | MARC 2-4
Transport Group Supervisor | LOCAL or EMS C | EMS C | MARC 2-4
Trasport Group to Ambulances | LOCAL or IFERN | IFERN | IFERN2
Medical Control | LOCAL or EMS A/B | EMS A or B | Wiscom EMS
Air Ambulance LZ | MARC 2 | MARC 2 | EMS C

## Slide 18: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
How to sector hot zone radio communications
Unit Assignment | Routine Local Incidents | MABAS Incidents | Alternative
DISPATCH / RESPONSE: |  |  | 
IC to the Local Dispatcher | Local Dispatch | IFERN | IFERN2
IC to the MABAS Dispatcher | IFERN | IFERN | IFERN2
Badger Red Center |  | MABAS1 (Wiscom) | STAC 1 (Wiscom)
Inter-Divisional Response |  | MABAS1 (Wiscom) | STAC 2-8 (Wiscom)
MABAS Regional Coordinators |  | MABAS2 (Wiscom) | STAC 2-8 (Wiscom)
Staging Officer – Intra-divisional |  | IFERN | IFERN2
Staging Officer - Interdivisional |  | MABAS1 | MABAS2

## Slide 19: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand Narrowbanding, and how it will affect you
  “Wideband”
  radio channels
  “Narrowband”
  radio channels
10
10
10
10

## Slide 20: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand Narrowbanding, and how it will affect you
  “Wideband”
  radio channels
  “Narrowband”
  radio channels
10
5
5
5
5
5
5
5
5
5
10
10
10

## Slide 21: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand Narrowbanding, and how it will affect you
  “Wideband”
  radio channels
  “Narrowband”
  radio channels
10
5
5
5
5
5
5
5
5
5
10
10
10

## Slide 22: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand Narrowbanding, and how it will affect you
  “Wideband”
  radio channels
  “Narrowband”
  radio channels
10
5
5
5
5
5
5
5
5
5
10
10
10

## Slide 23: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand Narrowbanding, and how it will affect you
  “Wideband”
  radio channels
  “Narrowband”
  radio channels
2 ½” Hose
v

## Slide 24: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand Narrowbanding, and how it will affect you
  “Wideband”
  radio channels
  “Narrowband”
  radio channels
2 ½” Hose
v
1 ½” Hose

## Slide 25: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand the difference between analog and digital communications channels, and how they can affect you
  Analog
  radio channels
  Digital
  radio channels
Spoken Voice
Radio Transmission
Listening

## Slide 26: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand the difference between analog and digital communications channels, and how they can affect you
  Analog
  radio channels
  Digital
  radio channels
Spoken Voice
Radio Transmission
Listening

## Slide 27: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand the difference between analog and digital communications channels, and how they can affect you
  Analog
  radio channels
  Digital
  radio channels
Spoken Voice
Radio Transmission
Listening
Encode
Decode
1000101110100100010100100101001010010101

## Slide 28: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand the difference between analog and digital communications channels, and how they can affect you
  Analog
  radio channels
  Digital
  radio channels
Spoken Voice
Radio Transmission
Listening
Encode
Decode
1000101110100100010100100101001010010101

## Slide 29: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Understand the difference between analog and digital communications channels, and how they can affect you
  Analog
  radio channels
  Digital
  radio channels
DIFFERENCES:
#1 Fade versus Signal Dropout (think cellphones)
#2 Realtime versus Digital Delay
#3 Variable audio quality versus Crisper Audio
DANGER OF USING DIGITAL IN TACTICAL SITUATIONS:
- The “Encoder” does not know the difference between
your voice and loud background noises

## Slide 30: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
608-757-0400

## Slide 31: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
Badger RED Center
MABAS-Wisconsin Answering Point
Notification Center vs Dispatch Point
    Stricken Division calls Badger Red Center
    Badger Red Center notifies Division Coordinator/
      State Fire Service Coordinator
      WEM Duty Officer
      MABAS-WI President/Vice President
MABAS Representative Contacts Stricken Division
When to contact Badger RED Center?
    “Notification Call” when an incident reaches 3rd Alarm
    Whenever your Division needs interdivisional help

## Slide 32: MABAS Radio Operations (IFERN/IFERN2, WISCOM & Tactical Channels) and Badger RED Center
QUESTIONS?
DISCUSSION?
FEEDBACK?